## Slide 1: Aspects of reliability of a power system
 | Generation (+ load, DSM and storage) | Networks (T&D)
Adequacy | Sufficient firm capacity | Sufficient and reliable transport and distribution capacity
Security | Flexibility of the system Robustness to contingency including stability | Voltage control capability Robustness to contingency including stability
Generation from VRE generators is variable, uncertain, location-constrained, non-synchronous, and often distributed (connected to distribution grid).

## Slide 2: Technical properties of VRE and their impacts to the aspects of reliability
 | Generation (+ load, DSM and storage) | Networks (T&D)
Adequacy | Variability reduces contribution to firm capacity | Location-constraints may require grid extension and reinforcement
Security | Variability and limited predictability requires system to follow residual load Lack of inertia and governor response may pose the technical limit to VRE penetration | Location-constraints may change voltage control requirements Distribution level connection may affect voltages and protection system coordination RE’s behavior during fault may affect system stability

## Slide 3: Impacts on the total system costs
 | Generation (+ load, DSM and storage) | Networks (T&D)
Adequacy | More generation capacity would be needed | Transmission investment costs
Security | Cost for deploying flexibility measures Cost for device to provide inertia and governor response | Transmission and Distribution network enhancement (new lines and devises)
Flexibility measures include: ramping, demand side management, storage, trade