## Slide 1
Modeling
Systems Integration of
Variable
Renewable
Energies
in
IAMs
Robert Pietzcker
Potsdam Institute
for Climate Impact Research
Bonn, 2nd March 2015

## Slide 2: ADVANCE Project
Improve Integrated Assessment Models for better policy advising
Focus on
  Demand side
  Uncertainty
  Innovation and technological development
  Variable renewable energies
  Land-Water-Energy Nexus
  EU policies

## Slide 3: Integrated Assessment Models (IAMs)
Main goal: Create self-consistent long-term scenarios that inform about climate mitigation strategies
 Dynamic
 Endogenous dynamic resource prices
 Covering not only power, but all energy sectors
 Aggregated over space (countries, continents)
 Aggregate over time (timestep = 1-5 years)
Used to assist in policy making
Derive mid-term energy and capacity needs
Derive aggregated infrastructure investment needs (transport, grids)
Set midterm targets, e.g. renewable energy shares or emissions
 Not necessary to get individual power plants & grid lines right, but to represent aggregated integration challenges and effects!

## Slide 4: Challenge: Bridging the scales
Two main characteristics of VRE
Temporal variability
Heterogeneity in space
Modeling Challenge:
How to bridge the scales between
Reality IAM
Hourly fluctuations versus 5-year time steps
Irradiance differs on ~100km versus Continental scale
Chart: 
PVGIS © European Union, 2001-2012

## Slide 5: Participating models
IAMS:
AIM/CGE
IMAGE
MESSAGE
POLES
REMIND
WITCH
More detailed models:
REMIX
REEDS

## Slide 6: VRE integration in IAMs
Different examples from models (EMF 27 study, 2012)
No limits, no integration costs
Upper limits (e.g., max 30% VRE)
4 load bands
12*8 time slices
Integration cost markups
Strict backup requirement (x GW gas for each GW wind)

## Slide 7: Different approaches
MESSAGE (IIASA):
Capacity adequacy and flexibility equation
POLES:
Coupling to a limited hourly dispatch model
REMIND (PIK):
Integration costs markup rising with VRE share
Explicit Residual Load Duration Curves (RLDCs)

## Slide 8: MESSAGE: Sullivan appraoch
Capacity equation:
Purely technical
Wind/PV is counted with a capacity value that decreases stepwise as Wind/PV share increase
„Flexibility equation“:
Parameterized to represent both utilization and flexibility effect
Cannot be derived from technological parameters needs results from a more detailed model

## Slide 9: Strengths and weaknesses
Strengths:
Endogenously decreasing capacity adequacy captures the increase of integration challenge with VRE share
Simple equations
Weaknesses
Difficult to tailor system response with a single parameter
Needs results from more detailed model for reliable parameterization of flexibility Balance
Does not capture the positive interaction between wind and solar

## Slide 10: POLES: Coupling to reduced dispatch model
10

## Slide 11: POLES: Coupling to reduced dispatch model
11

## Slide 12: Strengths and weaknesses
Strengths:
Can show hourly balancing needs
Endogenous use of short-term storage
Weaknesses:
Depends very strongly on the choice of representative days – you need a good algorithm to choose these!
What is the feedback to the investement model? If realized full load hours are not fed back, system investment and operation are uncoordinated and very suboptimal
Impossible to integrate in an intertemporally optimizing model

## Slide 13: REMIND 1: Integration cost markups
13
Pietzcker, Stetter, Manger, Luderer (2014) „Using the sun to decarbonize the power sector: the economic potential of photovoltaics and concentrating solar power“

## Slide 14: REMIND 1: Integration cost markups
14
Basic idea of the approach:
Integration challenges increase with the share of each VRE
Variability can be reduced by storage, else results in curtailment
Parameters based on battery and H2 electrolysis costs, detailed modeling
Chart: 
| 0 | 7 | 12 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 52 | 55 | 60 | 64 | 70 | 75 | 80 | 85 | 90 | 95 | 100
PV | 0 | 0 | 8.6944 | 13.9111 | 22.6055 | 31.2999 | 39.9943 | 48.6887 | 57.3831 | 66.0775 | 78.2497 | 83.4663 | 92.1608 | 99.1163 | 109.5496 | 118.244 | 126.9384 | 135.6328 | 144.3272 | 153.0216 | 161.716
Pietzcker, Stetter, Manger, Luderer (2014) „Using the sun to decarbonize the power sector: the economic potential of photovoltaics and concentrating solar power“

## Slide 15: Resulting integration cost markups
15
Pietzcker, Stetter, Manger, Luderer (2014) „Using the sun to decarbonize the power sector: the economic potential of photovoltaics and concentrating solar power“
Chart: VRE share [%]
| 0 | 7 | 12 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 52 | 55 | 60 | 64 | 70 | 75 | 80 | 85 | 90 | 95 | 100
PV | 0 | 0 | 8.6944 | 13.9111 | 22.6055 | 31.2999 | 39.9943 | 48.6887 | 57.3831 | 66.0775 | 78.2497 | 83.4663 | 92.1608 | 99.1163 | 109.5496 | 118.244 | 126.9384 | 135.6328 | 144.3272 | 153.0216 | 161.716
Wind | 0 | 0 | 7.1173 | 11.3877 | 18.505 | 25.6224 | 32.7397 | 39.857 | 46.9743 | 54.0917 | 64.0559 | 68.3263 | 75.4436 | 81.1375 | 89.6783 | 96.7956 | 103.9129 | 111.0303 | 118.1476 | 125.2649 | 132.3822
CSP | 0 | 0 | 3.1273 | 5.0036 | 8.1309 | 11.2581 | 14.3854 | 17.5126 | 20.6399 | 23.7671 | 28.1453 | 30.0216 | 33.1489 | 35.6507 | 39.4034 | 42.5307 | 45.6579 | 48.7852 | 51.9124 | 55.0397 | 58.1669
Specific (per kWh)
Total (whole system)
Chart: VRE share [%]
| 0 | 7 | 12 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 52 | 55 | 60 | 64 | 70 | 75 | 80 | 85 | 90 | 95 | 100
PV | 0 | 0 | 2.2953 | 4.5906 | 9.9464 | 17.2149 | 26.3962 | 37.4903 | 50.4971 | 65.4167 | 89.5177 | 100.9943 | 121.6522 | 139.5557 | 168.7064 | 195.1026 | 223.4116 | 253.6334 | 285.7679 | 319.8152 | 355.7753
CSP | 0 | 0 | 0.8256 | 1.6512 | 3.5776 | 6.192 | 9.4943 | 13.4847 | 18.1631 | 23.5295 | 32.1982 | 36.3262 | 43.7566 | 50.1962 | 60.6813 | 70.1756 | 80.3579 | 91.2283 | 102.7866 | 115.0329 | 127.9673
Wind | 0 | 0 | 1.879 | 3.7579 | 8.1422 | 14.0923 | 21.6082 | 30.6899 | 41.3374 | 53.5507 | 73.28 | 82.6748 | 99.5856 | 114.2416 | 138.1046 | 159.7128 | 182.8868 | 207.6266 | 233.9322 | 261.8037 | 291.2409
Value of VRE electricity, @60$/MWh | 0 | 18.48 | 31.68 | 39.6 | 52.8 | 66 | 79.2 | 92.4 | 105.6 | 118.8 | 137.28 | 145.2 | 158.4 | 168.96 | 184.8 | 198 | 211.2 | 224.4 | 237.6 | 250.8 | 264

## Slide 16: Strengths and weaknesses
Strengths:
Captures that integration challenges increase with VRE share
Simple equations
Easy to differentiate between regions
Weaknesses:
Needs results from more detailed model for reliable parameterization
Does not reflect negative effect of VRE on utilization of dispatchable plants

## Slide 17: REMIND 2: RLDC approach
Ueckerdt et al (subm.) „Representing power sector variability and the integration of variable renewables in long-term climate change mitigation scenarios: A novel modeling approach “

## Slide 18: Regional time series
Load (normalized)
Hours of a year
Hours of a year
Wind power
Solar PV
USA
India

## Slide 19: RLDCs show three major integration challenges
Residual load curve
25% wind, 25% PV, India
Variable
renewables
Reduced cap. factor
Low capacity credit
Overproduction
Dispatchable
plants
Residual load duration curve
Load (normalized)
Load (normalized)
Hours of a year (sorted)
Hours of a year

## Slide 20: Implementing RLDCs in IAMs
Time (sorted)
Load
Base Load
Mid Load 1
Mid Load 2
Ueckerdt et al. “Representing power sector variability and the integration of variable renewables in long-term climate change mitigation scenarios: A novel modeling approach”. (submitted)
8760 FLh
6000 FLh
100 FLh
2000 FLh

## Slide 21: Implementing RLDCs in IAMs
Time (sorted)
Load
Base Load
Mid Load 1
Mid Load 2
Peak
Add 40% wind
8760 FLh
6000 FLh
100 FLh
2000 FLh

## Slide 22: How the RLDC data was developped
Input:
Hourly time series for wind onshore and PV production, aggregated over respective region (provided by DLR)
Hourly time series for demand
DIMES: „Dispatch & Investment Model for Electricity Storage”
  Takes VRE-shares as given
  Optimizes residual power system, including short-term storage (Batteries)
  Hourly model for economic dispatch
  Uses resource costs similar to 2050 values in IAMs (same as REMIX)
  150$/tCO2
  Mark-up on storage costs to better recreate REMIX EU results
Output:
Residual Load Duration Curve before/after short-term storage
Cost-optimal storage
Curtailment

## Slide 23: Using the RLDC data: Capacity Adequacy
Fit the residual peak capacity as function of wind/PV share
3rd order polynomial in wind and solar share

## Slide 24: Using the RLDC data: Curtailment
Fit curtailment as function of wind/PV share
3rd order polynomial in wind and solar share

## Slide 25: Differences accross regions - peak
EU
USA
MEA
At low VRE shares, situation in MEA and EU seem similar
At high shares, peak load reduction achieved in MEA from solar+storage are larger

## Slide 26: Differences accross regions - curtailment
EU
USA
MEA
If there is a well-developed grid connecting the whole region, there is only minimal curtailment <5% up to VRE shares of 40%

## Slide 27: Strengths and weaknesses
Strengths:
Captures the correlation between load, wind and solar explicitly
Utilization effect of dispatchable plants is fully included in the model
Weaknesses:
High quality data needed for parameterization
Difficult to include the effect of coupling macro-regions
To capture short-term storage effects, a more detailed model is needed for data preparation

## Slide 28: Summary
IAMs are used to set mid- and long-term targets
IAMs need to get the big picture right:
  how large are integration challenges
  what are interactions between different technologies
  What are additional investment needs for flexibility (grid, storage, demand side)
In ADVANCE, we developed several new approaches for representing VRE challenges in IAMs
  Capacity and flexibility equations
  Integration cost markups
  Coupling to reduced dispatch model
  Explicit RLDC representation
The more detailed a modeling approach is, the higher the requirements on data (load & VRE time series)

## Slide 29: Backup

## Slide 30: Backup

## Slide 31: REMIND 1: Integration cost markups
31
Solar electricity costs (US, climate policy)
Photovoltaics
Concentrating Solar Power
Electricity costs [$/MWh]

## Slide 32: Regional differences in RLDCs
Solar PV
Wind
India
USA
Hours of a year (sorted)
Residual load/peak load
Hours of a year (sorted)

## Slide 33: Effect of short-term storage on RLDCs
India 50% solar PV
Hours of a year (sorted)
Residual load/peak load